If your existing fireplace has a gas valve that interferes with the mantel leg, please follow the instructions below to drill through the leg.

When dry fitting the mantel and legs, mark a line on the wall next to each side of the leg. Take the leg down and measure the distance from both sides to the center of the valve and then from the floor/hearth to the center of the valve. Next, transfer those measurements to the leg, identifying the center of the hole you will need to drill. Unscrew the escutcheon plate to use as a template for the hole. Scribe a line around the escutcheon. Using a small masonry drill bit, drill holes as close together as possible along the line just drawn (usually in a circle). Then tap gently with a hammer in the center of the circle just drilled to break the stone. Remove the pieces of stone to reveal the foam core. Find the corresponding center on the back of the leg and repeat the process. Once the stone is removed use a key hole saw or a long screwdriver to dig out the foam core to allow a clear passage way for the key used to operate the gas valve. You will probably need to buy a longer key to turn the gas on and off. Using the sanded caulk, apply a small bead around the back of the escutcheon and press into to hole.