# Mantel Installation Instructions

(Page one)

    - Remove old fireplace mantel (if applicable)

    - Ensure surface is smooth and free from dust and debris

    - Assemble all required tools and products necessary for installation (see list)

    - Dry-fit Mission Stone  mantel

      - Ensure legs are plum

      - Level mantel

      - Check that sufficient space exists between fireplace opening  and Mission Stone  surround

      - Make sure you follow all local building and fire codes

|  | Use a pencil to mark a line on the wall to use as a guide when installing mantel surround Take Mission Stone mantel down Re-verify with 6’ level, that links are plum and level |
| --- | --- |
|  | Use liquid nails Construction adhesive With a ¼” opening in tip of tube apply to one leg Press firmly against wall and floor (hearth) ensuring leg is aligned with plum line |

# Mantel Installation Instructions

(Page two)

|  | Follow adhesive manufacturer’s recommendations for use Repeat process for second leg Allow time to dry Apply adhesive to top of both legs Apply adhesive to mantel back |
| --- | --- |
|  | Lift mantel into place and press firmly to wall and down on legs Check for level Allow time to dry Use a 1 x 2 to firmly press mantel to wall (remove after 24-48 hrs) Use sanded caulk and apply a ⅛” bead where mantel and legs meet wall |
|  | Wipe with a wet finger to ensure a smooth bead Wipe wall and mantel clean with a damp sponge. |